3340 VCO
Possible 3340 VCO design ideas:
Base mainly on existing designs… Hybrid of LMNC and Kassutronics? (T. Henry VCO Maximus maybe, but original design doesn’t translate well to ±12V; see Fonitronik and Modularsynthesis.com versions for 12V modifications)
# Modifications from Kassutronics:
## Fairly definite:
  - Add protection diodes
  - No +5V regulator. Kassutronics limits internal pitch CV (center value, Frequency, and Fine Tune) to 0–5V, using a regulator instead of a voltage reference for some reason, but we will not.
  - Replace CV sources with LMNC ones: Octave switch, center trimmer, fine tune knob (center detent?), V/Oct CV in, attenuated CV in. Expand octave switch to 8 octaves.
  - Add LMNC style link? Maybe not identical, but something for my own controller?
  - Access to trimmers and measurement point from front
With foregoing modifications we have this panel:
  - Pots: (4) CV, Fine tune, PW, PWM CV
  - Rotary switch: (1) Octave
  - Toggle switch: (1) Soft/hard sync
  - Jacks: (5 in) V/Oct, CV, Lin FM, PWM, Sync; (4 out) Sine, Tri, Ramp, Pulse
  - Trimmer holes: (6) Tracking, Center freq, HFT, Sin shape, Sin amp, Voltage ref
  - Measurement point hole: (1) Vref
## Also consider:
- Note the LMNC VCO is said to produce ~ 440 Hz at CV of 9 V; at 12 V it tops out about 3100 Hz. I don’t understand why this is so low. Per the CEM3340 datasheet, with 1 nF cap on pin 11 it should have a useful range about 5 Hz to 10 kHz (with 15 V supply, but for the same CV range, 12 V should get only ~25% higher frequencies). Perhaps this is with summed CVs going higher than is possible with a 12 V system. I’d like higher frequencies than 3100 Hz, so perhaps the cap should be lowered. Note the Electrosmith ES 3340 module claims a frequency range of 0.045 Hz to 100 kHz, with CV from -7.5 V to +12V.
- Don’t use 3340 pulse wave output; instead use comparator on triangle(?) wave. This due to known problems with 3340 pulse wave: Oscillations on falling edge, frequency changes with PWM, and bad pulse shape at high frequency.
- Or do use pulse wave output, but add the Latvian Solution http://www.alfarzpp.lv/eng/sc/AS3340%20tip%20VCO%20_%20PWM%20.pdf and pulse reshaping https://lookmumnocomputer.discourse.group/t/1222-tuner-vco-module-fixes-improvements/2072/7?u=analogoutput .
# Kassutronics compared to LMNC
  - LMNC uses internal Zener for VEE. K uses -5V regulator.
  - LMNC uses +12V for freq trimmer and PW knob, 4.1V(?) voltage reference for octave switch and to get 1V for fine tuning. K uses +5V regulator for freq, PW, and fine tuning knobs.
  - K uses both hard and soft sync, LMNC uses hard only
  - K adds 10n cap between 470R resistor on pin 13 and ground
  - LMNC uses ~2x resistances for high freq track
  - K CVs are:
    - +5V / 220k fixed CV
    - 0–+5V / 47k frequency knob
    - 0–+5V / 1.5M fine tune knob
    - 2x Input / 100k V/Oct jacks
  - LMNC CVs are:
    - 0–+12V / 100k frequency center trimmer
    - +4/+3/+2/+1/0V / 100k octave switch
    - 0–+1V / 100k fine tune knob
    - Input / 100k pot / 470k modulation CV jack
    - Input / 100k V/Oct jack
  - LMNC PWM section is more complicated, provides both manual PW and PWM CV with attenuation. K provides only CV with attenuation (normalled to +5V for manual control if no CV)
  - K provides Tri-Sin converter for Sin output
  - K amplifies all outputs for 10Vpp
  - LMNC provides link connector